These are my notes on different types of ATARI controllers.
I decided to put them together after I read a posting by Mark Howard about
the steering controllers and trackball on some ATARI 8-bit page.

Joysticks
---------

     circuital diagram pin assignments
     ----------------- ---------------
        ___________
    org blk \5 4 3 2 1/
     | | \9_8_7_6/
     O-----+
        | wht
        | | pin wire
        +-----O # col function
        | -----------------
        +-----\ 1 wht ^ (up)
        | | 2 blu v (down)
      grn -O +-----O- bwn 3 grn < (left)
        | 4 bwn > (right)
        | 6 org fire
        | (7 red +5V) (*)
        O 8 blk GND
        |
        blu (*) only used in joysticks
        with autofire switch

     autofire circuit
     ----------------

        red firing frequency:
        |
        /----------+ f=1,44/[(R1+2*R2)*C]
        | |
        Z /--+ ( T=0,694*(R1+2*R2)*C )
      R1 Z .__|__|__.
        | | 8 4 |
        +----7 | typical values:
        | | 3----- org
        Z | LM 555 | C1=0,42 nF
      R2 Z /-6 5----\ R1=10 K
        | | | | | R2=10 K
        +--+-2 | = C1 C=100 nF
        | |___1____| |
        | | | (These are the values I selected.)
        \---||---+---------/
        C |
        blk

Paddles
-------

     circuital diagram pin assignments
     ----------------- ---------------
        ___________
        pushbutton R \5 4 3 2 1/
        __I__ /---NNN-- \9_8_7_6/
        o o | ^
        | | | | pin wire
     L grn blk yel vio # col function
    ------------------------------------ -----------------
     R bwn blk yel red 3 grn L button
        4 bwn R button
        5 red R paddle
        R=1M 7 yel +5V
        (R=500K for Commodore) 8 blk GND
        9 vio L paddle

Keyboard controllers/Video touch pad
------------------------------------

     circuital diagram pin assignments
     ----------------- ---------------
        ___________
     grn vio wht blu \5 4 3 2 1/
      | | | | \9_8_7_6/
      +-NN-+-NN-+ |
      | R R | | pin wire
      O---------O---------O----- bwn # col function
      | | | -----------------
      | | | 1 bwn row 1
      O---------O---------O----- red 2 red row 2
      | | | 3 org row 3
      | | | 4 yel row 4
      O---------O---------O----- org 5 grn col 1
      | | | 6 blu col 3
      | | | 7 vio +5V
      O---------O---------O----- yel 9 wht col 2

        R=4,7K

     Readings
     --------

     The following program appeared in COMPUTE!, 2/87, "Readers Feedback"
     section, page 30. It allows to read a keyboard controller (or video
     touch pad, since they are internally identical) connected to port 1:

     1 GRAPHICS 0
     10 DIM ROW(3),I$(13),BUTTON$(1)
     30 GOSUB 6000
     60 POSITION 2,7:PRINT "CONTROLLER # 1:";
     80 GOSUB 7000:POSITION 19,7:PRINT BUTTON$;
     120 GOTO 80
     6000 REM
     6010 POKE 54018,48:POKE 54016,255:POKE 54018,52:POKE 54016,221
     6030 ROW(0)=238:ROW(1)=221:ROW(2)=187:ROW(3)=119
     6040 I$=" 123456789*0#"
     6050 RETURN
     7000 PORT=54016
     7010 P=1:PAD=0
     7020 FOR J=0 TO 3
     7030 POKE PORT, ROW(J)
     7040 FOR I=1 TO 10:NEXT I
     7050 IF PADDLE(PAD+1)>10 THEN P=J+J+J+2:GOTO 7090
     7060 IF PADDLE(PAD)>10 THEN P=J+J+J+3:GOTO 7090
     7070 IF STRIG(0)=0 THEN P=J+J+J+4:GOTO 7090
     7080 NEXT J
     7090 BUTTON$=I$(P,P)
     7100 RETURN

STM1 Mouse
----------

     circuital diagram pin assignments
     ----------------- ---------------
        ___________
     (Are you nuts? It consists of \5 4 3 2 1/
      23 resistors, 2 capacitors, \9_8_7_6/
      2 movement sensors and an
      LM 339N quad-comparator IC!) pin wire
        # col function
      Well, at least the buttons: -----------------
        1 bwn L/R sense
        L button R button 2 org L/R reference
        __I__ __I__ 3 grn U/D sense
        o o o o 4 blu U/D reference
        | | | | 6 yel L button
        yel blk wht blk 7 red +5V
        8 blk GND
        9 wht R button

     readings
     --------

     The STM1 Mouse works as an inverted trackball (which is, in fact, what
     it is). The left button corresponds to the joystick trigger; the right
     button must be read in more or less the same way as the keyboard
     controllers, I guess (I had to return the mouse I borrowed before
     finishing my analysis).

     Mouse rolling forwards (up) Mouse rolling backwards (down)

        U/D U/D U/D U/D
        REF SNS REF SNS
        ------- -------
        0 1 0 0
        1 1 <-\ 1 0 <-\
        0 1 --/ 0 0 --/
        ... ...

     Mouse rolling left Mouse rolling right

        L/R L/R L/R L/R
        REF SNS REF SNS
        ------- -------
        0 1 0 0
        1 1 <-\ 1 0 <-\
        0 1 --/ 0 0 --/
        ... ...

     I tried to write a resident handler which should convert the mouse
     readings into joystick values and put them into the shadow register
     for joystick 2 (remember that on the ATARI XL/XE only joysticks 0
     and 1 are in effect, and 2 & 3 just contain repeats of 0 and 1).
     Then, if you read STICK(2), you would have the translated values;
     STRIG(2) would give you the status of the right mouse button; and
     for the left button, you would still use STRIG(0). Unfortunately,
     the routine got hanged sooner or later, and I had to return the
     borrowed mouse before I could finish debugging it. Maybe I can
     borrow another and resume the task...

     Marco Antonio Checa Funcke
     Botoneros 270
     Lima 33
     Peru

     (formerly reachable at jtkirk@urp.edu.pe
      but currently without an own account;
      however, postmast@urp.edu.pe is a close
      friend...)